PAM2011: Lecture 9 Problem Sheet Solutions

- State the two principle laws of electromagnetism

Faraday’s Law: An electric current is induced to flow in a circuit if some part of the circuit is in a changing magnetic field

Lenz’s Law: The induced current flows in a direction such that it opposes the action that induces it.

- There are 125 turns on the primary side, Np, of a transformer and 90,000 turns on the secondary side, Ns. If 110 V (ac) is supplied to the primary winding, Vp, what will the voltage induced in the secondary winding, Vs?

79.2 KV

- Describe the process of mutual induction

Mutual induction is the generation of an alternating current in a secondary coil by supplying an alternating current to the primary coil

process of inducing a current

- Why is it necessary to use a commutator ring in a DC motor?

Changes direction of current flow during cycle of motor – changes DC current into AC

- Why is an iron core generally used in an electromagnet?

Iron has a higher magnetic permeability than air and therefore intensifies magnetic field inside core